## Slide 1
HOW GPU
DIFFERS FROM CPU
HOW GPU
DIFFERS FROM CPU
ONE SMART BOSS vs THOUSANDS OF WORKERS

## Slide 2
1
2
3
Our Journey Today
02 • COMPUTER SYSTEMS
Our Journey Today
Processor basics
Meet CPU
Meet GPU
Compare
Teamwork
Quiz
Click any stop to jump straight there

## Slide 3
Warm-up: Who Would You Hire?
03 • COMPUTER SYSTEMS
Warm-up: Who Would You Hire?
ONE GENIUS
Solve one very hard puzzle
1,000 HELPERS
Colour 1,000 identical drawings
That choice is the whole story of CPU vs GPU.

## Slide 4
What Is a Processor Really?
04 • COMPUTER SYSTEMS
What Is a Processor Really?
INPUT
receive data
PROCESS
follow instructions
OUTPUT
produce result
Every app = millions of tiny instructions: add • compare • move
GHz is the drummer’s beat — billions of ticks each second.

## Slide 5
Meet the CPU: The Head Chef
05 • COMPUTER SYSTEMS
Meet the CPU: The Head Chef
CENTRAL
PROCESSING
UNIT
The general-purpose brain: a few powerful cores that make decisions, handle surprises, run apps, operate the OS, and manage the whole machine.

## Slide 6
Inside the CPU
06 • COMPUTER SYSTEMS
Inside the CPU
CONTROL UNIT
Reads + directs
ALU
Maths + logic
REGISTERS
Tiny fast notebooks
CACHE
Close, fast memory
FETCH → DECODE → EXECUTE → REPEAT
Example instruction: 2 + 3

## Slide 7
Cores, Threads & Pipelines
07 • COMPUTER SYSTEMS
Cores, Threads & Pipelines
1 CORE
one chef
4 CORES
4 chefs
8 CORES
8 chefs
THREADS
One chef switches quickly between two jobs.
PIPELINING
An assembly line: the next instruction starts early.
BRANCH PREDICTION
The chef guesses the next step to avoid waiting.

## Slide 8
Meet the GPU: An Army of Line Cooks
08 • COMPUTER SYSTEMS
Meet the GPU: An Army of Line Cooks
GRAPHICS
PROCESSING
UNIT
Thousands of simple cores do the same kind of work together. Each core is modest; the combined throughput is enormous.
THOUSANDS → 10,000+ CORES

## Slide 9
Inside a GPU: SMs & Warps
09 • COMPUTER SYSTEMS
Inside a GPU: SMs & Warps
Zoom in, one layer at a time: chip → SM → warp → thread
GPU
The whole chip
Dozens to 100+ SMs sharing one big pool of VRAM
SM
Streaming Multiprocessor
A mini-processor: ~128 cores, registers, shared memory, warp schedulers
WARP
32 threads, 1 instruction
The unit the scheduler issues. All 32 move in lockstep
THREAD
One tiny worker
Handles one data item, like a single pixel
Example: RTX 4090 = 128 SMs × 128 cores = 16,384 CUDA cores
← Agenda
Click to reveal →

## Slide 10
Why Was the GPU Invented?
10 • COMPUTER SYSTEMS
Why Was the GPU Invented?
1920 × 1080
> 2 million pixels
× 60 refreshes each second
> 120 million tiny colour calculations every second
Repeated maths also powers AI.

## Slide 11
Big Idea: Serial vs Parallel
11 • COMPUTER SYSTEMS
Big Idea: Serial vs Parallel
1
2
3
4
5
6
GO
GO
GO
GO
GO
GO
SERIAL
PARALLEL
One ticket counter
LOW LATENCY
CPU strength
100 counters open
HIGH THROUGHPUT
GPU strength

## Slide 12
Different vs Same Together
12 • COMPUTER SYSTEMS
Different vs Same Together
CPU • MIMD
Different cores can do different jobs
GPU • SIMD / SIMT
One instruction, lots of data
Example: add 20 to every pixel
GPU threads march in teams called WARPS — usually 32 threads moving in lockstep.

## Slide 13
Latency Hiding: Never Idle
13 • COMPUTER SYSTEMS
Latency Hiding: Never Idle
Memory is slow. Watch how each processor deals with the wait.
CPU core
stalls and waits
RUN
WAIT: memory takes 100s of cycles
RUN
GPU SM
swaps to another warp
Warp A
Warp B
Warp C
Warp D
Warp A again
CPU strategy
Hide slow memory with big caches and smart branch prediction.
GPU strategy
Keep thousands of threads in flight. When one warp stalls, the scheduler issues another at almost no cost.
← Agenda
Click to reveal →

## Slide 14
Where Does the Chip Space Go?
14 • COMPUTER SYSTEMS
Where Does the Chip Space Go?
CPU
LARGE CONTROL LOGIC
BIG CACHE
FEW BIG ALUs
Silicon spent on management
GPU
MANY, MANY ALUs
SMALLER CONTROL
SMALLER CACHE
Silicon spent on workers

## Slide 15
REGISTERS
L1 / L2 / L3 CACHE
RAM / VRAM
STORAGE
Memory: Cache + RAM vs VRAM
15 • COMPUTER SYSTEMS
Memory: Cache + RAM vs VRAM
CPU: sports car — low delay for a few passengers
GPU VRAM: bus — huge bandwidth for thousands

## Slide 16
Memory: Latency vs Bandwidth
16 • COMPUTER SYSTEMS
Memory: Latency vs Bandwidth
Peak theoretical bandwidth of typical parts: how much data per second
CPU RAM
dual-channel DDR5
≈ 90 GB/s
Gaming GPU
GDDR6X, RTX 4090
≈ 1,000 GB/s
Data-centre GPU
HBM3, H100
≈ 3,350 GB/s
PCIe: the narrow bridge
PCIe 4.0 ×16 moves only ≈ 32 GB/s between CPU RAM and VRAM. Copy once, compute a lot.
Coalescing
Neighbouring threads read neighbouring addresses, so 32 small reads merge into one wide fetch.
← Agenda
Click to reveal →

## Slide 17
Worked Example: Add 1,000,000 Numbers
17 • COMPUTER SYSTEMS
Worked Example: Add 1,000,000 Numbers
CPU
~125,000 additions per core, step by step
GPU
Each core gets a few additions; thousands run together
THINK: what if every step needs the previous result?

## Slide 18
CPU Loop vs GPU Kernel
18 • COMPUTER SYSTEMS
CPU Loop vs GPU Kernel
CPU: one loop
for (int i = 0; i < N; i++) {
c[i] = a[i] + b[i];
}
Visits the items one after another.
GPU: one thread per item
__global__ void add(a, b, c, N) {
int i = blockIdx.x * blockDim.x
+ threadIdx.x;
if (i < N) c[i] = a[i] + b[i];
}
Thread i handles item i. All threads launch together.
Thread ID = blockIdx × blockDim + threadIdx: a seat number for every worker
← Agenda
Click to reveal →

## Slide 19
When the GPU Does NOT Help
19 • COMPUTER SYSTEMS
When the GPU Does NOT Help
DEPENDENT STEPS
One result must wait for another
BRANCH DIVERGENCE
If/else makes warp members wait
SMALL TASKS
PCIe copying costs more than it saves
Amdahl’s idea: parallel speedup is limited by the part that must stay serial — like a group project waiting on one person.

## Slide 20
Amdahl’s Law: Try the Numbers
20 • COMPUTER SYSTEMS
Amdahl’s Law: Try the Numbers
Speedup = 1 / ((1 − p) + p / N)
p = share of the work that can run in parallel • N = 1,000 cores
50% parallel
≈ 2× (limit 2×)
90% parallel
≈ 9.9× (limit 10×)
95% parallel
≈ 19.6× (limit 20×)
99% parallel
≈ 91× (limit 100×)
Even 5% serial work caps 1,000 cores at about 20×.
← Agenda
Click to reveal →

## Slide 21
CPU vs GPU: Side by Side
21 • COMPUTER SYSTEMS
CPU vs GPU: Side by Side
Full form
Central Processing Unit
Graphics Processing Unit
Cores
Few powerful
Thousands simple
Best at
Decisions + serial work
Repeated parallel maths
Goal
Low latency
High throughput
Memory
RAM + large caches
VRAM + high bandwidth
Style
Flexible MIMD
SIMD / SIMT
Typical
OS, apps, files
Graphics, AI, simulation
Analogy
Head chef
Army of line cooks

## Slide 22
Where They Are Used in Real Life
22 • COMPUTER SYSTEMS
Where They Are Used in Real Life
Operating system
Gaming + video
Web + spreadsheets
3D animation
Compile code
AI training
File handling
Science + weather
CPU
GPU
Tensor cores are specialised GPU units for matrix maths.

## Slide 23
Better Together: CPU + GPU Workflow
23 • COMPUTER SYSTEMS
Better Together: CPU + GPU Workflow
1
Program starts
on CPU
2
CPU prepares
data
3
Copy to GPU
memory
4
GPU computes
in parallel
5
Results return
to CPU
Integrated GPU: inside the same chip • Dedicated GPU: a separate card
The CPU still conducts the whole system.

## Slide 24
Pick the Processor!
24 • COMPUTER SYSTEMS
Pick the Processor!
Decide first, then click to see the answer.
SCENARIO 1
Filter a 4K video: the same colour tweak on 8 million pixels
GPU
Same maths on every pixel is pure data parallelism.
SCENARIO 2
Decide which of 20 menu items the user just clicked
CPU
Small, branchy, one-off decisions: low latency wins.
SCENARIO 3
Train a neural network: billions of multiply-adds
GPU
Matrix maths suits thousands of cores plus tensor cores.
SCENARIO 4
Add up 10 numbers, just once
CPU
Too small: copying over PCIe costs more than the maths.
← Agenda
Click to reveal →

## Slide 25
Quiz Time!!
25 • COMPUTER SYSTEMS
Quiz Time!!
1 Which has more cores?
GPU
2 Which runs the operating system?
CPU
3 What is VRAM?
GPU’s own fast memory
4 What is a warp?
32 threads in lockstep
5 Is a GPU always faster?
False

## Slide 26
THANK YOU!
Questions?
CPU
few smart cores • low latency • flexible boss
GPU
thousands of simple cores • high throughput • parallel muscle
Neither is better. They are partners.